## Slide 1: Jacob Summer Update II
Design Parameters

## Slide 2: Overview
To build a dynamic robot capable of balancing and hopping
Incorporate force measurement device
Begin with hopping 2dof leg
Use simulation to inform design

## Slide 3: Literature
Penn Jerboa
  tail driven, passive spring legs
  control hip rotation of leg
  1.6 leg lengths hop height (+.6 above)
  kangaroo rat

## Slide 4: Tasks
Use Unity to:
  Model spring, joints, and contact
  Collect data
  Respond to feedback and actuate mechanism
  Enable interaction
Build simulation of leg
Use simulation to:
  Select leg dimensions
  Determine spring characteristics
  Select motors
Manufacture first prototype
Design harness
Manufacture harness
Write vertical hopping code
Test code in simulation
Test hopping with actual leg

## Slide 5: Progress
Base units
  Hectograms and centimeters
  Therefore, g = 981 cm/s^2 & spring constant in N/m is 1/10 game spring constant

## Slide 6: Progress
Determined spring parameters
  2 leg lengths hop height
  100-200 N/m
  130 N/m compresses to 10% of unstretched length when dropped from 2 leg lengths
  Each spring in device experiences 50-100% of force on foot

## Slide 7: Progress
Balancing
  Max 4.1 cm between masses with 4 cm foot & 2.2 cm with 2 cm foot
  How to attach foot?
    Limit

## Slide 8: Progress
Full model
  From script
  Problems with simulating motors