## Slide 1: Jacob Summer Update IV
Optimization

## Slide 2: Overview
To build a dynamic robot capable of balancing and hopping
Incorporate force measurement device
Begin with hopping 2dof leg
Use simulation to inform design

## Slide 3: Literature – R.S. Fearing
Power Modulation and Optimization

## Slide 4: Tasks
Use Unity to:
  Model spring, joints, and contact
  Collect data
  Respond to feedback and actuate mechanism
  Enable interaction
Build simulation of leg
Use simulation to:
  Select leg dimensions
  Determine spring characteristics
  Select motors
Manufacture first prototype
Design harness
Manufacture harness
Write vertical hopping code
Test code in simulation
Test hopping with actual leg

## Slide 5: Simulation MATLAB
  Moment arm vs jump height with
    100 rpm motor --> 1.02m moment arm and 1.447m jump height
    300 rpm motor --> .182m moment arm and .519m jump height
  Motor internal gear ratio vs jump height with
    .05m moment arm --> 668 rpm and .2995m
    .1m moment arm --> 432 rpm and .358m
  Small increase in motor speed results in large reduction of ideal moment arm
  Less leg-lengths of jump height for larger moment arm

## Slide 6: Simulation Unity
Iterate through lengths and gear ratios
Best gauge of height
Limit of moment arm length

## Slide 7: Motor